## Slide 2
More than 9,000 m2 of cutting-edge facilities
A technology centre with more than 30 years’ experience in the plastic sector.
What is
AIMPLAS?

## Slide 3
Solutions for Plastics
Technology
services
  1.
R&D&I
  2.
  3.
  Training and events

## Slide 4
New plastic recycling technologies: chemical, biological, enzymatic and thermal
17th June 2020
Chart: 
Pablo Ferrero Aguar
Chemical Recycling Group Member
(pferrero@aimplas.es)

## Slide 5
Chemical Recycling

## Slide 6
Chemical Recycling
It is a process where the polymeric chains are decomposed into petrochemical raw materials
Come back to the origin
Monomer
Infinite cycle
The recycling cycle can be carried out as many times as it is wanted without quality loosing
No material restriction
Almost every polymeric material can be chemically recycled under proper conditions and process
CHEMICAL
RECYCLING

## Slide 7
Chemical Recycling
Pyrolysis
Solvolysis
Biological/enzymatic degradation
Temperature (>400 degrees)
Inert atmosphere
Waste mixtures
Products: 3 fractions
Temperature, pressure and solvents
supercritical or subcritical conditions
Applicability of enzymes as biocatalyzers
Lower temperatures
Bioplastics and conventional plastics
TEMPERATURE
Technology Readiness Level

## Slide 8
Chemical Recycling
Pyrolysis
Solvolysis
Biological/enzymatic degradation
Temperature (>400 degrees)
Inert atmosphere
Waste mixtures
Products: 3 fractions
Temperature, pressure and solvents
supercritical or subcritical conditions
Aplicability of enzymes as biocatalyzers
Lower temperaturas
Bioplastics and conventional plastics
TEMPERATURE
Technology Readiness Level

## Slide 9
Chemical Recycling
Pyrolysis
Polymeric Chain
Heat
Pyrolytic reactions

## Slide 10
Chemical Recycling
Pyrolysis
Polymeric Chain
Heat
Pyrolytic reactions
Temperature increase
Products with shorter chain

## Slide 11
Chemical Recycling
Pyrolytic process
Feedstock
Solids
Pyrolytic oil
Gases
Heat exchanger
Pyrolysis reactor
G/L
Separator
Heat Generator

## Slide 12
Chemical Recycling
Classic Pyrolysis
Pyrolysis reactor
Heat
generator
Microwave assisted pyrolysis
Pyrolysis reactor
Microwave
generator
Microwave
absorber
Heat generation inside the reactor
More efficient process
Heat is generated outside the reactor
Less efficiency: Energy transfer

## Slide 13
Chemical Recycling
Related projects
LIFE ECOMETHYLAL

## Slide 14
Chemical Recycling
AIMPLAS
Services
Pilot plant
Technical advice
Feasibility studies
Process optimization
Fractions characterization

## Slide 15
Chemical Recycling
Pyrolysis
Solvolysis
Biological/enzymatic degradation
Temperature (>400 degrees)
Inert atmosphere
Waste mixtures
Products: 3 fractions
Temperature, pressure and solvents
supercritical or subcritical conditions
Applicability of enzymes as biocatalyzers
Lower temperatures
Bioplastics and conventional plastics
TEMPERATURE
Technology Readiness Level

## Slide 16
Chemical Recycling
Solvolysis
Use of solvents, temperature and pressure to carry out the reverse reaction of polymer formation
Depending on the used solvent
Methanolysis  Methanol
Glycolysis  Glycol
Hydrolysis  Water
Depending on the chemical agent used for the polymer escision different monomer or oligomers are obtained
Fibers recovery

## Slide 17
Chemical Recycling
Solvolysis

## Slide 18
Chemical Recycling
Related projects
Objective: to obtain new polyurethane foams for the raw materials (called green polyols) from polyurethane waste
Circular economy in polyurethane foams through chemical recycling

## Slide 19
Chemical Recycling
AIMPLAS
Services
Solvolysis reactor
Technical advice
Optimization process
Catalyzers development
Products characterization
New products development

## Slide 20
Chemical Recycling
Pyrolysis
Solvolysis
Biological/enzymatic degradation
Temperature (>400 degrees)
Inert atmosphere
Waste mixtures
Products: 3 fractions
Temperature, preasure and solvents
supercrítical or subcrítical conditions
Applicability of enzymes as biocatalyzers
Lower temperatures
Bioplastics and conventional plastics
TEMPERATURE
Technology Readiness Level

## Slide 21
Chemical Recycling
Biological/enzymatic degradation
Use of microorganisms to mineralize polymers to CO2 and water or biogas
Use of enzymes (biocatalyzers) to degrade polymers to monomers or oligomers
Depending on the enzyme used different monomers or oligomers are obtained

## Slide 22
Chemical Recycling
Biological/enzymatic degradation
Polyester resin before degradation
Polyester resin after degradation

## Slide 23
Chemical Recycling
Polyurethane film before degradation
Polyurethane film after degradation
Biological/enzymatic degradation

## Slide 24
Chemical Recycling
Biological/enzymatic degradation
PHB film degradation
Chart: Degradation (%)
| 0 | 5 | 6 | 7
 | 0 | 63.0435 | 87.3043 | 92.7826

## Slide 25
Chemical Recycling
Conventional composting process
Result: Not successful biodegradation
due to low polymer degraders concentration
Polymer to degrade
Microorganisms not
degrading polymers
Microorganisms
degrading polymers

## Slide 26
Chemical Recycling
Polymer to degrade
Microorganisms not
degrading polymers
Microorganisms
degrading polymers
Improved process: bioaugmentation
Polymer degraders
addition
Result:
Successful biodegradation

## Slide 27
Chemical Recycling
Related projects
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 870292.

## Slide 28: AIMPLAS’ TRAINING ACTIVITIES
AIMPLAS, through its website AIMPLAS PLASTICS ACADEMY, offers you training activities adapted to your needs.
Click on the link to find the solution that best suits your interests.
  For more information visit our site
  www.aimplas.net/plasticsacademy
  or send an email at formacion@aimplas.es